Competition Rules

FSR

2011

V-H-O

Amendments, Additions and proposals for improvements are to

be directed to the NAVIGA Section Management via the representative of the Country, last date two months before a

World Championship.

Incase of doubt of the interpretation of the Rules and Regulations

the English text will be prevail.

The NAVIGA Executive Committee

CONTENTS:										Page:

1. DEFINITION OF MODELS									4

2. CLASSES											     4-5-6

3. PRINCIPAL AND GENERAL RULES							7

3.1 PRINCIPAL RULE										7

3.1.1. 	Competitions where the rules apply								7

3.1.2. 	Entree Fees											7

3.1.3. 	Protest Fees											7

3.2  PERSONAL RULES										7

3.2.1. 	Age groups											7

3.2.2. 	Competitors registration							     		8

3.2.3. 	Maximum allowed number of competitor							8

3.2.4. 	Assistant and substitution of the competitor							8

3.3 TECHNIICAL RULES										9

3.3.1. 	Propulsion of models and propulsion agents (fuel)						9

3.3.2. 	Fuels												9

3.3.3. 	Noise reductio, noise level measurement and rules						9

3.3.4. 	Methods for measuring noise levels in the FSR-V/H/O category				9

3.3.5. 	General 									       	      9 -10

3.3.6. 	Application and use of radio control equipment and frequenty control			10

3.3.7. 	Buoys (dimensios, construction and materials)						10

3.3.8. 	Starting pontoon ( construction and materials)				      	       10-11

3.3.9. 	Lapcounting and time measuring								11

3.3.10.Transponder mounting									11

3.3.11.	Transponder counting										11

3.4 SPORT RULES											12

3.4.1. 	The competition area										12

3.4.2. 	Starting area, preparation area and access permision			      	      12-13

3.4.3. 	Allowed number, entries and condition of models						14

3.4.4. 	Registrationnumbers										14

3.4.5. 	Registration of competitors and models							15

3.4.6. 	Issuing of starting permits, issuing start and computer passes				15

3.4.7. 	Surrender of competitor passes and assessment of running order				16

3.4.8. 	Calling time (time allowed to get ready)							16

3.4.9.	Preparation times (at the starting point)							16

3.4.10. Interruption – Suspension of the competition						16

3.4.11. Re-run of a race										16

3.4.12.	Unfair behavior										17

3.4.13. Scoring and announcement of the results							17

3.4.14. Checking of the first three placed models during World and	 	      	      17-18

Continental Championships

3.4.15. Awarding of titles at World and Continental Championships				18

3.4.16. Award ceremonies at World and Continental Championships				18

3.4.17. Result list											19

3.5 NAVIGA PROTEST POLICY									19

3.5.1.	Principal rules											19

3.5.2.	Lodging of protest										19

3.5.3.	Handling of protest										20

3.6 GENERAL RULES REGARDING CONSTRUCTION FOR CATEGORY FSR 	20

4. GENERAL RULES REGARDING THE SET UP OF COMPETITION			20

COURSES FOR FSR CATEGORY

5. GENERAL RULES REGARDING START AND TERMINATION OF A			20

RACE OR HEAT

6. COMPETITION REQUIREMENTS IN FSR CATEGORY					21

6.1.	General construction rules and regulations							21

6.2.	Manning level of the start pontoon								22

7. APPENDIX 1:											22

8. FSR V COMPETITION COURSE AND DURATION OF THE RACE			23

8.1.	Drawing 3											23

8.2.	Procedure for races in the FSR-V classes						      23-24

8.3.	Rules for over taking									 24-25-26

8.4.	Penalties in FSR-V classes									26

8.5.	Basic rules in the FSR-V classes								27

8.6.	Scoring in FSR-V classes									28

8.7.	Composition of result lists in the FSR-V classes						28

9. FSR H COMPETITION COURSE AND DURATION OF THE RACE			29

9.1.	Drawing 4											29

9.2.	Start clock for FSR-H classes							      29-30

9.3.	Procedure for races in the FSR-H classes						      30-31

9.4.	Basic rules and penalties in the FSR-H classes						32

9.4.1.	Left turns											32

9.4.2.	Right of way											32

9.4.3.	Negotiating – Passing the buoys							      32-33

9.5.	Rules for overtaking in the FSR-H classes						      33-34

9.6.	Calculation of final results in FSR-H classes						35

9.7.	Composition of results lists in the FSR-H classes						35  10. FSR O COMPITITION COURSE AND DURATION OF THE RACE			36

10.1.	Drawing 5											36

10.2.	Start clock for FSR-O classes							      36-37

10.3.	Procedures for races in the FSR-O classes 						37-38-39

10.4.	Basic rules and Penalties in the FSR-O classes					      39-40

10.4.1.	Left turns											40

10.4.2.	Right of way											40

10.4.3.	Negotiating – Passing the buoys							      40-41

10.5.	Rules for overtaking in the FSR-O classes						      41-42

10.6.	Scoring in FSR-O classes									43

10.7.	Composition of results lists in the FSR-O classes						43

Competition rules for radio controlled models in categories FSR-V-H-O

1. Defenition of models:	Modell leírása:

Models in the FSR categories are controlled by the competitor using radio control.

These are model boats of free design, wich conform to the race requirements, however

should in form and design look like a boat.

Az FSR kategória modelljeit a versenyző távirányító készülékkel vezeti.

A modellek szabad tervezésűek figyelembe véve a verseny által támasztott követelményeket

valamint a modellnek hasonlóan kell kinéznie mint egy hajónak.

2. ClASS FSR-V 	FSR-V osztályok

The category FSR-V can be divided into the following groups:

Az FSR-V kategória az alábbi csoportokra van felosztva:

Class FSR-V 3.5	Free build racing models for endurance races (20-30 min.)

with internal combustion motor up to 3.5 cc and below

waterline propulsion.

Szabad építésű modellek a túra versenyzéshez (20-30 min.)

belsőégésű motorral szerelve. A motor lökettérfogata max.

3,5 ccm vízvonal alatti hajtással.

Class FSR-V 7.5	Free build racing models for endurance races (20-30 min.)

with internal combustion motors above 3.5 cc up to 7.5 cc

and below waterline propulsion.

Szabad építésű modellek a túra versenyzéshez (20-30 min.)

belsőégésű motorral szerelve. A motor lökettérfogata max.

3,5 - 7,5ccm között, vízvonal alatti hajtással.

Class FSR-V 15	Free build racing models for endurance races (20-30 min.)

with internal combustion motors above 7.5 cc up to 15 cc

and below waterline propulsion.

Szabad építésű modellek a túra versenyzéshez (20-30 min.)

belsőégésű motorral szerelve. A motor lökettérfogata max.

7,5 - 15ccm között, vízvonal alatti hajtással.

Class FSR-V 27	Free build racing models for endurance races (20-30 min.)

with internal combustion motors (petrol-motors with

sparkplug ignition) above 15 cc up to 27 cc and below

waterline propulsion.

Szabad építésű modellek a túra versenyzéshez (20-30 min.)

belsőégésű motorral szerelve.(benzin üzemű motor szikragyújtással)

A motor lökettérfogata max.15 - 27ccm között, vízvonal alatti hajtással.

Class FSR-V 35	Free build racing models for endurance races (20-30 min.)

with internal combustion motors (petrol-motors with

sparkplug ignition) above 27 cc up to 35 cc and below

waterline propulsion

Szabad építésű modellek a túra versenyzéshez (20-30 min.)

belsőégésű motorral szerelve.(benzin üzemű motor szikragyújtással)

A motor lökettérfogata max.27 – 35 ccm között, vízvonal alatti hajtással.

2.1. CLASS FSR-H	FSR-H osztályok

The category FSR-H can be divided into the following groups:

Az FSR-H kategória az alábbi csoportokra van felosztva:

Class FSR-H 3.5	Free build HYDRO – planes* with internal combustion motor

up to 3.5 cc and with surface drive propulsion.

Szabad építésű Hydro-planes* belsőégésű motorral szerelve.

Motor lökettérfogata max. 3,5 ccm vízfelületi hajtással.

Class FSR-H 7.5	Free build HYDRO – planes* with internal combustion motors

above 3.5 cc up to 7.5 cc and with surface drive propulsion.

Szabad építésű Hydro-planes* belsőégésű motorral szerelve.

Motor lökettérfogata 3,5 - 7,5 ccm között vízfelületi hajtással.

Class FSR-H 15	Free build HYDRO – planes* with internal combustion motors

above 7.5 cc up to 15 cc and with surface drive propulsion.

Szabad építésű Hydro-planes* belsőégésű motorral szerelve.

Motor lökettérfogata 7,5 - 15 ccm között vízfelületi hajtással.

Class FSR-H 27	Free build HYDRO – planes* with internal combustion motors

(petrol-motor with sparkplug ignition) above 15 cc up to 27 cc

and with surface propulsion.

Szabad építésű Hydro-planes* belsőégésű motorral szerelve.

Motor lökettérfogata 3,5 - 7,5 ccm között vízfelületi hajtással.

Remark:		* HYDRO – planes (A free build model with three ore more

planing surfaces)

Megjegyzés:		* HYDRO-planes (Szabad építésű modell három vagy több

tervezett úszó felülettel)

2.2. CLASS FSR-O	FSR-O osztályok

The category FSR-O can be devided into the following groups.

Az FSR-H kategória az alábbi csoportokra van felosztva:

Class FSR-3.5	Free build OFFSHORE boats with internal combustion motor

up to 3.5 cc and with surface drive propulsion.

Szabad építésű OFFSHORE hajók belsőégésű motorral. A motor

lökettérfogata max. 3,5 ccm vízfelületi hajtással.

Class FSR-7.5	Free build OFFSHORE boats with internal combustion motors

above 3.5 cc up to 7.5 cc and with surface drive propulsion.

Szabad építésű OFFSHORE hajók belsőégésű motorral. A motor

lökettérfogata 3,5 – 7,5 ccm között vízfelületi hajtással.

Class FSR-15		Free build OFFSHORE boats with internal combustion motors

above 7.5 cc up to 15 cc and with surface drive propulsion.

Szabad építésű OFFSHORE hajók belsőégésű motorral. A motor

lökettérfogata 7,5 – 15 ccm között vízfelületi hajtással.

Class FSR-27		Free build OFFSHORE boats with internal combustion motors

(petrol-motors with sparkplug ignition) above 15 cc up to 27 cc and 				with surface drive propulsion.

Szabad építésű OFFSHORE hajók belsőégésű motorral.

(benzin üzemű motor szikra gyújtással) A motor

lökettérfogata 15 – 27 ccm között vízfelületi hajtással.

Class FSR-35		Free build OFFSHORE boats with internal combustion motors

(petrol-motors with sparkplug ignition) above 27 cc up to 35 cc and 				with surface drive propulsion.

Szabad építésű OFFSHORE hajók belsőégésű motorral.

(benzin üzemű motor szikra gyújtással) A motor

lökettérfogata 27 – 35 ccm között vízfelületi hajtással.

3. PRINCIPAL AND GENERAL RULES	LEGFONTOSABB ÉS ÁLTALÁNOS SZABÁLYOK

3.1.	Principal Rules	Legfontosabb szabályok

3.1.1.	Competitions where the rules apply	Versenyek ahol a szabályokat alkalmazni kell

(1)	World Championships	Világbajnokságok

Continental Championships	Kontinens bajnokságok

International Competitions	Nemzetközi versenyek

International Friendly Competitions	Nemzetközi Baráti versenyek

(2)	For countries associated with NAVIGA it is recommended, that they use this rules

in their national events.

A NAVIGA tagországoknak ajánlott ezen szabályok alkalmazása a saját nemzeti

rendezvényeiken is.

(3)	The year of the competition is from January 1” until January 1” of the next year.

A versenyévad január 1-től a következő év január 1-ig tart.

(4)	The organisation have to Pay for the judges:

Shelter and Food for the working days on World and Continentalchampionships

For the first 3 working days	 € 10 each day

For the other working  days	 €   5 each day

For International Competitions only Shelter and Food

Bírói díjak melyeket a rendező fizet.

Szállás és étkezés a munkanapokra Világ- és Kontinentális Bajnokságokon

- az első három napra 10 € / nap

- a további napokra 5 € / nap

Nemzetközi versenyeken csak szállás és étkezés

3.1.2.	Entry Fee	Nevezési díj

Entry Fees for official NAVIGA events are as follows:

Seniors € 20.00 per class. € 15.00 for organisers. € 5 for the section.

Juniors € 15.00 per class. € 10.00 for organisers. € 5 for the section.

Nevezési díjak a hivatalos NAVIGA rendezvényeken a következők:

Felnőtt 20 € / kategória. (15 € a rendezőnek, 5 € a szekciónak.)

Junior 15 € / kategória. (10 € a rendezőnek, 5 € a szekciónak.)

3.1.3.	Protest Fees	Óvási díj

The protest fee at all official NAVIGA competitions is € 10.

Az óvási díj minden hivatalos NAVIGA versenyen 10 €.

3.2.	Personal Rules	Személyekre vonatkozó szabályok

3.2.1.	Age Groups	Korcsoportok

At NAVIGA events the competitors are divided  into two Age Groups-Juniors

and Seniors.

(1)	A Junior is someone who in the year of the competion is not older than 18 years.

(A Junior is someone who in the year of the event does not have their 19” birtday)

(2)	For safety reasons the junior competitors in the FSR 15 cc engines classes must be

at last12 year old

(3)	Juniors are not allowed to take part in the FSR 27 cc and FSR 35 cc classes.

NAVIGA rendezvényeken a versenyzőket két csoportba kell besorolni, junior és

senior.

- Junior az a versenyző aki a verseny évében nem idősebb 18 évesnél.

(Junior az a versenyző aki a rendezvény évében nem töltötte be a 19 életévét.)

- Biztonági okokból a 15 ccm-es kategóriákban a junior versenyzőknek be kell tölteniük

a 12 életévüket.

- Az FSR 27 ccm-es és az FSR 35 ccm-es kategóriákban junior korú versenyző nem indulhat.

3.3.2.	Competitor registration	Verseny regisztráció

(1)	In order to compete in a championship or other international event an application

must be made country’s  association on behalf of the competitor.

(2)	The application should be received by Organisers in accordance with their terms

and can be refused if received late.

(3)	An association is only allowed to enter competitors if their country’s membership

subscriptions, as set by NAVIGA, have be payd.

(4)	By entering the competition the competitor accept the rules that apply.

- A Világbajnokságon vagy más nemzetközi versenyen a jelentkezési dokumentumot

az induló ország modellező szövetsége küldi el  a versenyző helyett.

- A rendezőknek a jelentkezési dokumentumokat időben meg kell kapniuk. A később

leadott jelentkezést vissza kell utasítani.

- Az a versenyző vehet részt a versenyen aki regisztrált tagja saját országának a

szövetségénél és az a szövetség befizette a tagdíjat a NAVIGA-nak.

- A versenyző elfogadja a versenyre kiírt szabályokat.

3.2.3.	Maximum Alowed Competitors	Maximum engedélyezett létszám

(1)	At the World Championships each country is allowed to enter the following number

of competitors in Senior and Junior:

(2)	In the FSR-V/H/O classes 3 competitors and the title defedant.

In the FSR-V/H/O classes it can be more, if one country have a competitor in the final

the country  have the right for 1 extra place in the next World Championship.

If they have 2 competitors in the final than they have 2 extra place’s for the next

World Championship, in this case they have the right  for 5 competitors, the maximum

is 5 competitors and the title defendant.

(3)	The host country (organizer from the world-championship) can enter 5 competitors and

the title defendant, but the maximum is 5 regardless of the result at the last championship.

(4)	At the Continental Championships each country is allowed to enter the following number

of competitors in Senior and Junior:

(5)	In the FSR-V/H/O classes 5 competitors and the title defenant.

In the FSR-V/H/O classes it can be more, if one country have a competitor in the final

the country have the right for 1 extra place in the next Continal Championship.

If they have 2 competitors in the final than they have 2 extra place’s for the next

Continental Championship, in this case they have the right for 5 competitors, the

maximum is 7 competitors and the title defendant.

- A világbajnokságon résztvevő országok a következő szempontok szerint nevezhetnek

versenyzőket a Junior és Senior kategóriákban.

- FSR-V/H/O kategóriákban 3-3 versenyző és a mindenkori védő.

Az FSR-V/H/O kategóriákban annak az országnak van lehetősége több versenyzőt nevezni

amelynek versenyzője a világbajnokság döntőjébe jutott és így 1 extra helyet szerzett az

adott országnak.

Amennyiben 2 versenyző jutott a döntőben, abban az esetben az adott ország 2 extra

hellyel rendelkezik a következő világbajnokságon. Egy ország maximum 5 versenyzőt

nevezhet és a mindenkori védőt.

- A rendező ország 5 versenyzőt nevezhet és a mindenkori védőt, de maximum 5 versenyzőt

függetlenül az előző világbajnokságon elért eredményektől.

- A kontinens bajnokságokon résztvevő országok a következő szempontok szerint nevezhetnek versenyzőket a Junior és Senior kategóriákban.

- FSR-V/H/O kategóriákban 5 versenyző és a mindenkori védő.

Az FSR-V/H/O kategóriákban annak az országnak van lehetősége több versenyzőt nevezni

amelynek versenyzője az előző kontinens bajnokság döntőjébe jutott és így 1 extra helyet szerzett az adott országnak.

Amennyiben 2 versenyző jutott a döntőben, abban az esetben az adott ország 2 extra

hellyel rendelkezik a következő kontinens bajnokságon. Egy ország maximum 5 versenyzőt

nevezhet, de maximum 7 versenyzőt és a mindenkori védőt.

3.2.4.	Assistants and substitution of the competitor	A versenyzők helyettesítése és segítők

(1)	In each class a competitor is allowed to have an assistant who will be designated by

the competitor.

(2)	Tha assistant is allowed to help the competitor in the preparations for the start and

until the finish of the race.

(3)	Substitution of the competitor is NOT allowed during the race.

- Minden kategóriában megengedett egy segítő kijelölése, akit a versenyző jelöl ki.

- A segítőnek megengedett, hogy segítsen a versenyzőnek a verseny előkészítésében,

a starttól a verseny befejezéséig.

- A versenyző helyettesítése (csere) nem megengedett a verseny ideje alatt.

3.3.	Technical rules	Technikai szabályok

3.3.1	Propulsion of models and fuel	Modellek meghajtása és üzemanyaga

(1)	Only internal combustion motors are allowed. Jet engines and other forms of non

standardised propulsion are not allowed.

- Erőforrásként csak belsőégésű motorok használhatók. Jet hajtóművek és egyéb más

megoldások nem engedélyezettek.

3.3.2.	Fuel	Üzemanyag

(1)	Free fuel is allowed except in the FSR 27 cc and 35 cc class.

(2)	Fuel in the FSR 27 cc and 35 cc class must be a petrol-oil mixture. Petrol can be

of any octane level.

The use of Methanol mixtures is prohibited.

- Szabad üzemanyag használat engedélyezett kivéve a 27 ccm és a 35 ccm kategóriákat

- Az FSR 27 ccm-es és az FSR 35 ccm-es kategóriákban benzin-olaj keveréket kell

használni. Metanol-keverék üzemanyag nem használható.

3.3.3.	Noise reduction, noise level measurment and rules	Zajcsökkentés, zajszint mérés

(1)	Internal combustion engines must be equipped with a device to reduce noise levels.

(2)	The equipment used to assess the noise level shall not exceed approx. 0.3 dB and must

be in accordance with EEC and analoque rules. Noise level indicator issued by a

recognised authority, must be readily available.

(3)	If for noise level measurements, self-registration equipment is used, these should

reflect the measurments of the noise level indicator without too many differences.

It is therefore recommended that a comparison between the equipment in use should

take place. The comparison has to be checked by the Jury or the Organisers at the

start of the event/race and maintained throughout.

(4)	Noise level readings should be taken by individuals who have been trained

appropriately and have practical experience.

(5)	The noise meter should be set on “ SLOW ”.

- A belsőégésű motorokat el kell látni hatásos zajcsillapítással, hangtompítóval.

- Zajszint mérő berendezést kell használni amely 0,3 dB érzékenységű és megfelel az

EEC valamint az ezzel kapcsolatos előírásoknak. A zajszint mérő műszernek egy ismert

gyártótól kell származnia, aki azonnal elérhető. A szervezőknek biztosítania kell egy hatóságilag jóváhagyott zajszint jelző (ami ezek szerint nem azonos a zajszint mérővel?).

- Amennyiben a zajszint mérésére használt berendezés nem rendelkezik hatóság általi referenciával, az ezzel mért eredményeket érdemes összevetni a zajszint jelzővel(?) Az összevetés eredményét a bírók és a szervezők a verseny kezdetekor ellenőrzik, és megbizonyosodnak róla, hogy a verseny ideje alatt az esetleges eltérés változatlan marad.?

- Zajszint mérésre olyan embereket kell felkérni, akik megfelelő ismerettel és

gyakorlattal rendelkeznek a berendezés kezelésében.

- A zajszint mérőt “SLOW”-ra kell állítani.

3.3.4.	Methods for measuring noise levels in the FSR-V/H/O category	Zajszint mérési módszerek az FSR-V/H/O kategóriában

3.3.5.	General	Általános

(1)	The measurement microphone must be positioned as follows:

Height 100 cm. Approx.X 20 cm. Above water level.

Position 25 metres to the right for FSR-V and to the left for FSR-H/O at the right angle

to the centre line of the FSR course and 22 metres away from the line connecting the

two lowest buoys and securely attached.

(2)	At last three noise level measurments must be taken for each model during the race,under

the following conditions.

(3)	There should be no other boat within 15 metres arround the model being measured.

The noise measurement must be taken when the boat is on the base line at last 15 metres

away from the microphone.

The measurements must be evenly spaced durig the race.

(4)	The competitor must be advised immediately if their boat exceeds 80 dB/A. If the second

measurement also exceed the noise level they will receive a warning and if the third

measurement exceed thenoise level they will be immediately disqualified.

- A mérő mikrofon elhelyezése:

Magasság 100 cm a vízszint felett.

- Végül minden modellnek három mérési eredménnyel kell rendelkeznie

a verseny ideje alatt, a következő feltételekkel.

- A mért modell 15 méteres körzetében nem lehet másik modell.

A mérést akkor kell végezni amikor a modell az alapvonalon van 15 méter távolságra a

zajszint mérő berendezés mikrofonjától.

A méréseket a verseny alatt egyenlő időszakokra kell osztani.

- A versenyzővel azonnal közölni kell, ha a modell zajszintja meghaladja a 80dB-t.
Ha a második mérés eredménye is eltér a megengedett értéktől, akkor figyelmeztetni kell.

Amennyiben a harmadik mérés eredménye sem megfelelő a versenyzőt azonnal ki kell zárni

a futamból.

3.3.6.	Application and use of radio control equipment and frequency control	Rádiótávvezérlő berendezés alkalmazása és frekvencia kontrol

(1)	During official NAVIGA events only digital and proportial operated radio

control equipment is allowed. The radio control be capable of working within

10 kHz, the use of any other frequency bands may be possible.

(2)	It must be posible to change frequency at short notice. Each competitor must

have four different pairs of crystals.

(3)	The use of the radio control equipment is subject to the regulations of the country

where the NAVIGA event is held. Organisers must list the available frequencies

in the entry form.

(4)	It is recommended that frequency checks are carried out to avoid frequency clashes.

At World and Continal Championships there must be frequency checks.

(5)	The re-run of a race due to radio problems can be refused by the race officials,

if the planned finishing time of a race or championships is seriously endangered.

(6)	The frequncies must be recorded in MHz only.

(7)	Radio’s may not switched on within 1000 metres of the competition area.

Competitors who dissobey the rules will be disqualified from the whole competition.

- Hivatalos NAVIGA rendezvényeken csak digitális és proprcionális rendszerű

távirányító berendezések használata engedélyezett.

A távirányító berendezés legyen alkalmas 10 kHz-en belüli sávon dolgozni, de használható

bármely más lehetséges frekvencia tartomány.

- Képesnek kell lennie a frekvencia megváltoztatására. Minden versenyzőnek 4 pár eltérő

kristállyal kell rendelkeznie.

- A rádióberendezés használat szabályainak meg kell felelnie a rendező ország

ide vonatkozó előírásinak. A rendezőknek fel kell sorolniuk az ide vonatkozó szabályokat

a versenykiírásban.

- Javasolt a frekvencia ellenőrzés a lehetséges frekvenciaütközések elkerülése végett.

Világ- és kontinens bajnokságokon a frekvencia ellenőrzés kötelező.

- Egy futam újra futását rádióproblémák miatt elutasíthatja a versenyigazgatóság,

ha az időben veszélyezteti a verseny tervezett befejezését.

- Frekvenciát csak MHz-ben lehet megadni illetve regisztrálni.

- A versenyterület 1000 méteres körzetében nem lehet bekapcsolva rádióberendezés.

Amelyik versenyző ezt a szabályt megszegi azt véglegesen kizárják a versenyből.

3.3.7.	Buoys dimensions, Constuction, Anchorage	Bólya méretei, felépítése, rögzítése

(1)	The race course has to be marked by buoys. Each buoy must be concist of two colours

and have good visible coloured stripes. The buoys have to anchored so that they are

at a right angle to the water surface.

(2)	The buoys must be cylindrical and  minimum of 20 cm. and maximum 50 cm. above

the water surface.The buoys must be 40 cm.to 50 cm. in diameter.

(3)	The bouys must be made of materials such as polystyrene, or natural fibres, etc.

- A pálya vonalát bólyákkal kell megjelölni. Minden bólyát két különböző színű jól látható

csíkokkal kell megjelölni. A bólyát úgy kell rögzíteni, hogy merőleges legyen a

vízfelületre.

- A bólyának hengeres alakúnak kell lenni, mely átmérője 40 – 50 cm között lehet.

A bólyának a vízből 20 – 50 cm-re kell kiállnia.

- A bólyák anyaga lehet polisztirol..stb.

3.3.8.	Starting pontoon, Construction and Materials	A starthely, felépítése, anyaga

(1)	Starting pontoons have to provide adequate space for the competitors, their model,

assistants and judges. Any obstructions which could endanger the safety of the

competitor and models should be avoided.

(2)	The starting pontoon must be a minimum of 13 x 1.5 metres wide  and 19.5 metres long.

(3	Access to the starting pontoon should be clear. The surface of the pontoon must be

non slip even when wet.

(4)	The starting pontoon should when occupied not move, rol or in any way change position.

The surface of the starting pontoon must not be higher than 50 cm. above the water surface.

(5)	Floating starting pontoons are only allowed when the anchoring and stability are

sufficient to prevent rolling caused by waves or movement of people.

- A starthelynek (stég) megfelelő helyet kell biztosítania a versenyzőknek, azok modelljeik,

segítőik és a versenybírók számára. Kerülni kell minden olyan eszközt, felépítményt

amely veszélyezteti a versenyzők, segítőik biztonságát.

- A starthelynek minimum 13x1,5 méter hosszúnak kell lennie, de ajánlott a 19,5 méter.

- Biztosítani kell a starthely akadálymentes megközelítését. A starthely felületének

csúszásmentesnek kell lennie vizes állapotban is.

- A stég nem mozoghat, nem fordulhat el, nem változtathat pozíciót.

A stég felszíne a víz felszínétől nem lehet magasabban 50 cm-nél.

- Úszó stég akkor engedélyezett, ha úgy rögzíthető, hogy a hullámzás vagy a versenyzők mozgása nem forgatja azt el.

3.3.9.	Lapcounting	Körszámlálás

(1)	World Championships – Continental Championships – International events can only

count by Transponder counting.

- Világbajnokságon, kontinens bajnokságon, nemzetközi rendezvényen csak

transzponderes számlálás megengedett.

3.3.10.	Transponder mounting FSR-V/H/O	Transzponder tartó FSR-V/H/O

(1)	The transponder should not be more than 25 cm. from the back of the boat.

- A traszponder nem lehet 25 cm-nél távolabb a hajó farától (tükörtől).

3.3.11.	Transponder Counting FSR-V/H/O.	Körszámlálás FSR-V/H/O

(1)	For lap counting only 2 or 3 operators of the counting equipment and 1 or 2

announcers are needed.

(2)	The announcers and operators work in pairs and will be responsible for counting

the models. The announcers will cal the number of the model is passing the finishing

line and the lap will be recorded by the counting equipment operator.

(3)	Lap counters will only do the lap counting. Any lap deductions will be recorded by

the assistant pontoon judges and will be deducted (FSR-V/O classes) from the total

of laps recorded by the lap counters at the end of the heat.

(4)	There is only one finish line for all models FSR-V/H/O. The finish line is located on

the left hand side from the pontoon. The lap counters will be located in a raised

position in line with the finish line.

(5)	In the event of equal number of laps, the competitor whose model passed the finish

line first, will be the winner. A competitor with the start position number higher

than 1 can only be the winner, if they have overtaken all models in the start numbers

lower than them.

(6)	If  boats stopped before the end of final, the last passing from the finish line is the

finishing time.

Example:

Boat 1 have 68 Laps 30.12.1.

Boat 2 have 66 Laps 28.36.3.

Boat 3 have 66 Laps 29.12.8.

Boat 2 have the second place (better time) and boat 3 have place three.

The time should be measured to a 0,01 second.

- Körszámlálásra az adott berendezéshez 2 – 3 fő operátorra és 1 – 2 fő adminisztrátorra (bemondó) van szükség.

- A bemondó és az operátorok párban dolgoznak és felelősek a körszámlálásért. A bemondó hívja a be a versenyzőket a startszámok szerint és irányítja az elvonulást ahogy az operátor rögzítette a megtett körszámokat.

- A körszámláló operátor csak a körszámlálást végzi. Körlevonásra a starthely vezető bíró ad utasítást.Ezek a körszámok a futam alatt megtett össz körszámból lesznek levonva a futam után.(FSR-V/O)

- Csak egy célvonal van minden modell számára. (FSR-V/H/O). A célvonal a starthely (stég) bal oldalán kerül kiépítésre. A körszámlálók egy emelt helyen a célvonallal egyvonalban helyezkednek el.

- Egyenlő körszám esetén az a versenyző nyer, akinek modellje előbb hagyta el a a célvonalat. Az a versenyző akinek a startszáma nagyobb 1-nél csak akkor tud győzni, ha megelőz minden modellt, amelynek startszáma alacsonyabb a saját startszámánal.

- Ha a modell megáll mielőtt a futamnak vége lenne, akkor a utolsó ideje a befutó idő.

példa:

1 hajó 68 kör 30.12.1

2 hajó 66 kör 28.36.3

3 hajó 66 kör 29.12.8

A 2-es hajó végzett a második helyen (rövidebb idővel) és a 3-as hajó a harmadik.

Az időt 0,01 másodperces pontossággal kell mérni.

3.4.	SPORT RULES	SPORT SZABÁLYOK

3.4.1.	The Competition Area	A verseny terület

(1)	The competiton site especially the racing water  and the surrounding area should be

selected by the organisers to give competitors the best possible conditions to achieve

good results.

(2)	The organisers must ensure that adequate safety measures are in place to project

competitors, officials and spectators from possible dangers.

(3)	The competition site, the racing water and surrounding area must be checked prior

to the race by the race officials. In the event of complaints the organisers must

attempt to correct this immediately.

(4)	The competion site and the water must not be contaminated by mineral oils, grease

and other poisonous substances.

(5)	Failure to comply with this rule will result in disqualification of the competitor, who

will not able to lodge a protest.

- A verseny területét különösen a vízfelületre és az azt körülvevő területre úgy kell kiválasztania a rendezőnek, hogy az biztosítsa minden versenyzőnek a lehet legjobb feltételeket a jó eredmény eléréséhez.

- A szervezőknek biztosítaniuk kell a biztonságos elhelyezést a versenyzők, rendezők és nézők számára.

- A verseny területet, vízfelületet, környező területet a versenyigazgatóságnak kell ellenőrizni.

A felmerült problémákat azonnal ki kell javítani.

- A verseny területét és a vizet nem szabad szennyezni olajjal, zsírral vagy egyébb környezetszennyező anyaggal.

- Aki ezt a szabályt nem tartja be azt kizárják a versenyből. A kizárás ellen nem lehet óvást benyújtani.

3.4.2.	Starting area, the preparation and access permission.	Starthely, felkészülési terület és a belépés engedélyezése

(1)	The starting are is the enclosed area directly adjacent to the racing water,in wich the

starting pontoon is located from which the competitors launched their model.

(2)	The preparation area is an enclosed area, where all competitors prepare the models

and equipment for the start and serves as a waiting area during the event.

(3)	The preparation area should be located as close as possible to the starting area, subject

to local facilities. It should provide accommodation and protection from weather

conditions for the models. Only officials, competitors and assistants engaged in the

event are allowed in the preparation area.

(4)	The minimum requirements for a starting area in the class FSR-V/H/O category are.

One starting pontoon this should be minimum 19.5 meters long and 1.5 meters wide.

With numbered starting positions:

Class FSR-V from place 12 till 1.

Class FSR-H from place 1 till 8.

Class FSR-O from place 1 till 10.

(5)	Tables and chairs for the judges possibly protected from the weather.

1 Noise meter.

3 Yellow cards one with the number 1, one with the number 2, one with S (safety) on it.

1 Red card.

1 Signal device to indicate the Start/Finish of the heat.

1 Computer – clock to indicate the racing time.

1 Public address system.

2 Sets of number plates with the numbers 1 to 12.

1 Board with the drawing of the repective FSR course.

(6)	On the starting pontoon it is prohibited to use umbrellas during the race.

(7)	The organiser has to provide 2 rescue boats, 1 powered rescue boat and spare rescue boat.

The powered rescue boat must be stationed on the right hand side for the FSR-V class.

FSR-H/O classes the rescue boat must be stationed on the left hand site.

The crew for the rescue boat have to be provided by the organiser.

(8)	Inflatable boats, and other boats which could be demaged on inpact and endanger

the live of the crew, are not allowed to  be used as rescue boat. The crew of the rescue

boat must wear life jackets. If the protective suites are not live belts, the rescue boats

must be equipped with safety boards, wich should be mounted on the outside to

prevent damage.

(9)	The rescue service FSR-V is controlled by a start positon official.The model must be

rescued in the shortest posible time, causing minimum disturbance to the models still

racing ensuring that all the competitors are treated fairly.Powered rescue boats must

be used slowly, so that the bow waves have no adverse influence on the race.

The continuous circling of  rescue boat within the cours should be avoided. The

powered rescue boat should preferably be used to rescue those models wich are

farthest from the start jetty.

(10)	FSR-V boats must have a proper lifting point, in order to ensure a quick rescue.

(11)	FSR-V/O 27cc and 35cc boats must have a towing eye on the front for rescue purposes.

(12)	In classes FSR-H/O the rescue of models is only performed after completion of the heat.

Rescue from a boat in the FSR-H/O durend the race, only with a special permision

from the judge (if a boat is zinc).

(13)	The starting pontoon has to be divided into approximately 1.5 metre sections for

each competitor. The starting positions must be numbered and allocated prior to

the race. FSR – starting pontoons must have a board in front to prevent boats

landing on the pontoon.

(14)	At World and Continental Championships of the FSR group, the organiser must

provide a 1 metre high platform as part of the starting pontoon for the competitors

to drive from.

(15)	The raised platform must also numbered with starting positions. The competitor

is left the choice from which level they wish to drive. The competitor and assistant

can only use the allocated starting position.

(16)	Safety nets or other safety devices must be positionet around the competition site

to avoid endangering spectators. This should take into consideration models that

might collide or come of course.

(17)	During the race no body is allowed in the water. Competitors not obeying this rule

will be disqualified.

(18)	It is prohibited	, to run engines within 200 metres around (only with the radio out)

the starting pontoon.

- A starthely egy zárt terület, amely közvetlen érintkezésben van a vízfelülettel és magába foglalja a stéget amelyen a versenyzők elindítják modelljeiket.

- A felkészülési terület egy zárt terület, ahol minden versenyző előkészíti modelljét és felszerelését a startra valamint várakozik a váltásra.

- A felkészülési területnek elkülönítettnek kell lennie a starthelytől. Ennek biztosítania kell a védelmet az időjárástól a modellek részére. Csak rendezők, versenyzők és azok segítői tartózkodhatnak ezen a területen.

- Minimum követelmények a stéggel szemben az FSR-V/H/O kategóriákban. A stégnek minimum 19,5 méter hosszúnak és 1,5 méter szélesnek kell lennie. A starthelyeket a következők szerint kell megszámozni:

FSR-V 12-től 1-ig.

FSR-H 1-től 8-ig.

FSR-O 1-től 10-ig.

- Asztalok és székek a versenybíróknak, lehetőleg védve az időjárástól.

1 db zajszint mérő

3 db sárgalap. 1db 1-es számú felirattal, 1db 2-es számú felirattal, 1db S (safety) felirattal.

1 db piroslap

1 db hangjelző berendezés, mellyel a futamok kezdetét és végét jelzi a versenybíró.

1 db digitális óra, amely jelzi a versenyben eltelt időt.

1 db starthely beosztás

2 készlet startszám tábla 1-12-ig számozva

1 db tábla az FSR pálya (V és O/H) rajzával

- A verseny ideje alatt a stégen esernyő használata nem megengedett.

- A szervezőknek biztosítaniuk kell 2 mentőcsónakot. Egy motoros csónakot és egy tartalék csónakot. A motoros csónaknak az FSR-V versenyek ideje alatt a stég jobb oldalán, FSR-H/O versenyek alatt a stég bal oldalán kell tartózkodnia. A mentőcsónak személyzetét a rendező biztosítja.

- Felfújható és más hasonló szerkezetű csónakok, amelyek veszélyeztetik a személyzet életét nem használhatók mentőcsónakként. A személyzetnek mentőmellényt kell viselnie. Mentőmellény hiányában a csónakot oldalsó védőpalánkokkal kell felszerelni.

- A mentőcsónak személyzetének a munkáját a starthely vezető bíró irányítja. A modellt a lehető legrövidebb időn belül ki kell hozni. A mentőcsónak sebességét úgy kell megválasztani, hogy az ne keltsen indokolatlanul nagy hullámokat. Biztosítsa a sportszerű sportszerű versenyzést a többi versenyző részére. A mentést lehetőleg a legmesszebb leállt modellel kell kezdeni. Kerülni kell a mentőcsónak folyamatos mozgását.

- Az FSR-V hajókat fel kell szerelni fogantyúval a gyors mentés érdekében.

- Az FSR-H/O 27ccm és 35ccm-es modelleket egy vontatószemmel kell felszerelni a mentés érdekében

- FSR-H/O kategóriákban a mentés csak a futam befejezése után kezdődik meg. Amennyiben egy hajó süllyedni kezd, a versenybíró külön engedélyével a futam közben is menthető.

- A stéget fel kell osztani és lehetőleg minden versenyző részére biztosítani kell 1,5 méteres szakaszt. A starthelyeket számmal kell ellátni. A stég első részét védőráccsal kell biztosítani, hogy a modellek ne tudjanak feljutni oda.

- Világ- és kontinens bajnokságokon a rendezőnek biztosítínia kell egy 1 méter magas emelvényt, ahonnan a versenyzők vezethetik modelljeiket.

- Az emelvényt is meg kell számozni a starthelynek megfelelően. A versenyző dönti el, hogy melyik szintről vezeti modelljét. A versenyző és segítője csak ugyanazt a szintet használhatja.

- Biztonsági hálóval vagy egyéb védőeszközzel védeni a nézőket a versenypálya körül. Figyelembe kell venni a modellek haladási irányát.

- A verseny alatt a vízben tartózkodni tilos. Azt a versenyzőt aki ennek nem tesz eleget, kizárják a versenyből.

- Tilos motort járatni a starthely 200 méteres körzetében a verseny alatt. (kivétel, ha a rádió ki van kapcsolva)

3.4.3.	Allowed number, entries and condition of model.

(1)	Entry of a boat to other classes is not allowed. (V can only run in V classes, H only in

H classes and Offshore only in offshore classes).

(2)	In the category FSR each competitor can register for the event two models per class.

(3)	It is the choice of the competitor wich of the two models he will use for a race.

Both models can be brought into the preparation area. However, only one model can

be taken on the starting pontoon. The model what is on the pontoon can not more be

change for that heat. After start radio control (frequenty) and closing

radio control it is not posible to change crystals or repair other radio problems and take

part on that heat.

(4)	Each model must from start to finish of the event show the condition in witch it has

been originally registered. If during the start a part is miss or such a part has been

aded i.e. this part was lost during the race, this start will be without time i.e. without

a score registered. The dicision rest with start official.

(1)	Más kategóriához tartozó modellel a belépés nem megengedett. (V csak V osztályban, H	csak H osztályban és Offshore csak Offshore osztályban)

(2)	FSR kategóriában minden versenyző kettő modellt regisztrálhat kategóriánként.

(3)	A versenyző dönti el, hogy melyik modellt használja a versenyen. Mindkét modellt beviheti	az felkészülési helyre. A starthelyre csak egy modellt vihet. A modell a futam alatt nem cserélhető ki a másik modellel. A rádió ellenőrzés után már nem lehetséges kristályt cserélni vagy más javítást végezni a távirányítón.

(4)	Minden modellnek a regisztráción jóváhagyott állapotában kell lefutnia a versenyt a rajttól a futam végéig. Amennyiben a futam közben a modell egy darabja elveszik, a bíró döntése alapján a versenyző adott futambeli eredménye akár meg is semmisíthető.

3.4.4.	Registration Numbers   Regisztrációs szám

(1)	At all NAVIGA events all models must have fixed registration numbers.

(2)	The registration numbers are given out by the respective country. If the nationality

is not part of the registration number it must be attached to the models.

Registration numbers and nationality must not be changed and must permanently

Fixed on the hull.

(3)	The race and spare model must show an indentical registration numbers.

(4)	Boat-upper deck		XYZ	 = 	Nationality

H 3	 =	National Registration Number

(5)	Drawing 1: Boat registration number

- Minden NAVIGA rendezvényen minden modellnek rendelkeznie kell egy fix regisztrációs számmal.

- A regisztrációs számokat az adott ország modellező szövetsége adja. Ha egy nemzet nem tagja a NAVIGA szervezetnek, akkor a modellt el kell látni regisztrációs számmal. Regisztrációs számot és nemzetiséget nem lehet változtatni és fixen rögzíteni kell a modell fedélzetén.

- A verseny és tartalék modellt is el kell látni azonos regisztrációs számmal.

- A hajó felső fedélzeten 		XYZ = nemzetiség                                                                                                                                         a                                                            H3 = nemzeti regisztrációs szám

- A regisztrációs szám méretei.

3.4.5.	Registration of competitors and models Regisztráció (versenyző és modell)

(1)	Each competitor is required to register their models including any spare models and

their radio control equipment, within the registation time announced.

(2)	Together with models, the competitor must show the confirmation of their registration

issued by the organisers. Group confirmation should be shown by the team leader.

(3)	Qualified judges should be appointed by the organisers to carry out the registration.

These have to be confirmed by the jury of race officials.

(4)	The registrationmust be arranged by the organisers so that can be completed within the

set period, ensuring the planned start of the race and minimum disruption to competitors.

According to the number of registered competitors and models, marked registration

areas for various classes should be arranged.

(5)	The organisers must appoint sufficient qualified assistants.

(6)	The competitors must show their model for registration in the condition, in which it

will be used in the race.

(7)	The following items must be included in the registration list:

Surname-Cristian name of the competitor and their nationallity.

Class.

Registration number.

Specification of the radio equipment (frequency,modulation,working frequency,

spare crystals).

(8)	A marking on an appropriate place on the hull(shield,sticker,stamp, or similar)

must have affixed toe ach registered model.

The marking should not leave permanent stains on the outside of the model.

(1)	Minden versenyző köteles nyilvántartásba vetetni modelljét, beleértve a tartalék modellt és a

rádióberendezést is a regisztrációra kijelölt időben.

(2)	A versenyző és a modell regisztrációját rögzítenie kell a szervezőknek. A csapat regisztráción meg kell jelölni a csapat vezetőjét.

(3)	Minősített bírókat kell kijelölni a szervezőnek a regisztráció végrehajtására. Ezen személyek nevét meg kell adni a versenyigazgatóságnak.

(4)	A regisztrációt úgy kell szervezni a rendezőnek, hogy egy időben végre lehessen azt hajtani, ne befolyásolja a verseny kezdési időpontját. A különböző kategóriáknak külön helyet kell biztosítani a regisztrációhoz.

(5)	A rendezőnek megfelelően képzett segítőket kell kinevezni.

(6)	A versenyzőknek a modelljüket olyan állapotba kell bemutatniuk, ahogy azt a versenyen használni fogják.

(7)	A regisztrációs listának tartalmaznia kell:

- a versenyző neve és nemzetisége

- modell osztály

- regisztrációs szám

- a rádióberendezés specifikációja (frekvencia, moduláció, munka frekvencia, tartalék kristályok)

(8)	A regisztrált modellt meg kell jelölni a fedélzeten a hajó orrnál. (pajzs, matrica, bélyeg stb.)

A jelölés nem hagyhat maradandó nyomot a modellen.

3.4.6.	Issuing of starting permits, issuing start and competitors passed

Startengedélyek kiadása

(1)	After registration, the chiefjudge (at World and Continental Championships the jury)

must announce the start permission.

(2)	This must be done by public announcement giving the names of competitors and

classes entered. Reasons for refusalmust be given.

(3)	The competition or the championship can only start one hour after the announcement

of the starting permits.

(4)	The competior passes are to be issued by the organiser on the basis of the entries and

should be handed to the competitor at the time of registration.

(5)	The competitor must ensure that the enties on the competitor pass are correct.

The organisers must notified of any changes.

(6)	The Organiser i.e. the Duty Officer must issue the starting permits and ensure that

these are readily available  at the starting point.

- A regisztráció után a vezetőbírónak (Világ- és Kontinens Bajnokságon a versenyigazgatóság) be kell jelentei a startengedélyt.

- Ezt nyilvánosan meg kell tenni, megadva a verenyzők nevét és osztályát. Az elutasításokat meg kell indokolni.

- A verseny vagy a bajnokság kezdete ennek a listának a kifüggesztése után egy órával történhet.

- A versenyzőnek biztosítania kell, hogy az adatok megfelelnek a valóságnak. A változásokról a rendezőt értesíteni kell.

3.4.7.	Surrender of competitor passes and Assesment of Running Order

(1)	Prior to the race the competitor must hand in starting permit to the start official, failing

wich the competitor looses their permission to start that race.

(2)	The start sequence of the competitors at a starting point must be assessed prior to first the

race or lap per class under jurisdiction of the start position leader or other wise appoint

the available crystals. In the event additional races take place, the starting sequense must

be reversed.

(3)	The competition leaders or jury  can decise which frequencies are to be used at a certain

starting point.

(4)	If the competitor in the same event, competes in various model classes. There is no

possibility (right) to request a change of the starting time and/or a change of

starting sequence.

3.4.8.	Calling time (Time Allowed to Get Ready

(1)	The calling time is one minute. Within this time the start leader must call the competitor

three times by to show at the starting point.

(2)	If the competitor does not show up with his/her model within the calling time, the

competitor looses his/her right to start for this race or lap.

(3)	The competitor must 60 min before his start to be in the competiton area.

(if races fall out the competition can go on).

3.4.9.	Preparation times (at the Starting Point)

(1)	The finish of the preparation time must be announced verbally and possibly also optical.

3.4.10.	Interruption – suspensions of the competition

(1)	An interruption of the complete event can only be announced by the Chiefjudge.

(2)	An interruption of the competition at s starting pontoon is decided by the start

position official.

(3)	If a competition is suspended only the heats they are suspended have the right the rerun.

3.4.11.	Re-run of a race

(1)	There is no right to a re-run if the model is damaged during a race or if the propeller

is caught by a foreign object like weeds, pice of wood etc.

3.4.12.	Unfair behavior

(1)	In cases of unfair Behavior, interference (shout) with other competitors, judges, spectators, 	not following the rules, or exceptionally inconsiderate behavior of a competitor or mechanic 	it will be punished by disqualification (red card). The model has to taken out of the water.

There is no possibility of an appeal against the decision.

3.4.13.	Scoring and Announcement of the results

(1)	All results of a competitor should immediately be announced or displayed at the

starting area. The verbal announcement must be made in the English lanquage (this is the 	working lanquage in the Section FSR).

The verbal announcement is regarded as a provisional result.

(2)	The results are to be recorded in the result list. After the completion of the event the results

must be checked and made public within two hours. This is a preliminary result list.

(3)	The jury can confirm the final results one hour after issuing the preliminary results.

(4)	After confirmation of the results by the competitor officials i.e. jury, it is not longer

possible to protest against the results.

(5)	Competitors with a zero result will be recorded at the end of the result list in

alphabetical order.

3.4.14.	Checking of the first three placed models during World and Continal Championships

(1)	At World and Continal Championships the first three placed models must be checked

that they conform to the construction regulations and the engines are measured for

their true capacity.

(2)	In the FSR-V-H-O classes, with exception of the 27cc-35cc classes, preliminary checks

after the heats can be done to assess the exact capacity of the engines.

(3)	In the FSR – 27cc-35cc classes the measurement of the cylinder capacity of the first three

placed models is done on the basis of the constuction particulars after the completion

of the finals.

(4)	With internal combustion engines the measurement of the capacity must be done when

the engine is cold. A tolerance of + 1% is allowed.

(5)	Cylinder capacity measurements are done as follows:

The measurrement of the cylinder is done with a depth indicator through the glow/spark plug

hole. Only after this, the engine will be opened. The measurement of the bore is done with 	an inside measurement indicator in the region between the upper level of the exhaust

opening and the the top dead centre. Two measurements must be taken (approx. 90 degrees

opposite each other) and the results averaged.

Calibrators for the measurement instruments must be kept at the competition site.

The checking of the capacity measurements is done from tables or computer print outs.

During the qualification heats in the FSR-classes the start leader can select three models

for capacity checks. The measurement will be taken after the heat when the engines

have cooled down. Exceeding the allowed capacity means disqualification from that heat.

After completion of finals the models placed 1 to 4 will put a side. If not cylinder

capacity discrepancies are found for the first three placed models, further checks are

not necessary.

(6)	The competitors must make their model available to the appointed judge. The competitors

have to open the engine, failure to do so will result in disqualification.

(7)	In the event that the measurement results are not in accordance with the regulations,

the respective model will be disqualified. In that case the placing of the following

models will improve and they will have to be inspected.

3.4.15.	Awarding of titles at World and Continetal Championships

(1)	For juniors the World Championship title will be awarded , if a minimum of  6

competitors from 3 different countries have raced in the respective class.

(2)	For seniors the world Championships title will be awarded, if a minimum of 10

competitors from 5 different countries have raced in there repective class.

(3)	In case a World Championship for a certain class is held with less competitors

than described in paragraph (1) and (2), no titles and medals will be awarded in

those classes. The achievements of the competitors will be acknowledged by

special certificates.

3.4.16.	Award Ceremonies at World and Continental Championships

(1)	At World Championships the first three placed competitors in each class of  juniors

and seniors receive a gold, silver or bronze medal and a certificate, which are

provided by NAVIGA.

(2)	At Continental Championships the first three placed competitors in each class of

juniors and seniors received a gold, silver or bronze medal and a certificate.

(3)	In addition to the first three placed at World Championships each competitor recieves

a Certificate of attendance.

(4)	In addition to the title, medals and certificates, an honorary award can be given for

special achievements.

(5)	The title, medals, certificates and honorary awards must be presented in a public ceremony.

(6)	All competitors and officials must attend the prize giving ceremony. A competitor who

without a founded excuse does not attend the ceremony, looses the right to title, medals,

certificates and honorary award.The decission in respect of excuses rest with

the competition officials i.e. the jury.

3.4.17.	Result list

(1)	The organiser of a NAVIGA event must, after the completion of the event (ceremony),

give at least 3 complete rusult list to ach of the participating countries.

(2)	For special regulations regarding the contents of the result list refer to sections 7.6. for

FSR-V and 8.8. for FSR-H and 9.9. for FSR-O.

3.5.	NAVIGA- Protest Policy

3.5.1.	Principal rules

(1)	A protest can only be lodged, if a competitor is convinced that their race result has been

affected by a decision, act or omission made by the members of  the competition

management, the organiser or by unfair acts of other competiton or teams.

(2)	Protest against the judges-jury, or combined protest are excluded.

(3)	The final results, placing, the awarding of titles, medals and honorary awards can only

take place after all lodged protest have be resolved.

(4)	The decision of the jury is final. Appeals are not accepted.

3.5.2.	Lodgin of protests

(1)	Each protest must be verbally reported to the starting official immediately up on

observation of the alleged discrepancy. Within one hour after completion of the race in

which the incident occured, the protest must be lodged in writing to the competion

management e.g. the Jury in the English lanquage.

(2)	The lodging of a protest does not exclude the competitor from further participation

in the competition. If the competitor withdraws from further competition on grounds

of  a lodged protest, they will be disqualified from the whole event. In this case their

lodged protest will be rejected.

(3)	If after a verbally lodged protest measures are being taken to correct the situation a

written protest will not be necessary. The competitor must be advised prior to the

acceptance of the written protest and the protest fee.

(4)	The written protest must contain the following:

Grounds of protest (respective rules, regulations, acts and where to find them) time,

place including a precise description of the incident, the reason for the protest, possibly

including  drawings and other evidence. Statement and names of witnesses, who have

involved in the incident and are willing to truthfully answer questions regarding the protest.

Statement, with which start official and at what time, the protest was verbally lodged.

(5)	The protest must be signed by the competitor and the team leader of the respective country.

(6)	The protest fee must be paid when the written protest is lodged, or the protest will be

null and void.

3.5.3.	Handling of protest

(1)	The jury has to consider an officially lodged protest, from which the protest fee has been

paid and give a decision. During the protest negotiation the team leader of the country

whose competitor lodged a protest has no voting rights.

(2)	If during a protest a competitor is  accused to have breached the rules, the jury has to

carry out the protest procedure against the accused competitor.

(3)	The competitor who has lodged the protest and the person against whom the protest

negotiations are conducted, have the right to attend the hearing without voting rights.

For the protest negotiations the jury can call further witnesses involved in the incident

who must given a truthful account.

(4)	The decision given by the competiton management on the out come of the protest must be

announced to the competitors by means of a public notice in the English lanquage.

(5)	If the protest is successful the protest fee has to be returned to the competitor.

If the protest fails, the protest fee will remain with the organiser.

3.6.	General rules regarding construction for category FSR

(1)	For competions in category FSR models are of free design. The model however  must be	owned by the competitor.

(2)	The overall length of the model in the FSR category, must not exceed 2500 mm.

(3)	The steering of the model must be through radio control.

(4)	One or more internal combustion engines ca be used. However their total cylinder

capacity munst not exceed the respective class.

4.	General Rules regarding the set up of competition course or heat

(1)	Thecompetitions in the category FSR are performed on two different courses.

For the FSR-V category see drawing 3

For the FSR-H category see drawing 4

For the FSR-O category see drawing 5

(2)	The competition courses are to be placed, preferably in calm sheltered from wind, waters.

5.	General Rules regarding start and termination of a race or heat

(1)	During the competition the competitor is free to move within the clearly market area

allocated by the organizer on the starting pontoon.

(2)	After completion of the race or heat the model must be taken out of the water

immediality and radio control switched off.

6.	Competiton requirements in FSR category

6.1.	General constructions rules and regulations

(1)	The hull has no construction rules, however it must be in form and shape look like

a mono hull.

(2)	The engine must have full throttle control, a switch of  button is not allowed. The size

of the tank is not restricted. Fuel can to be supplied by the competitor.

(3)	Every model must have on the deck a longitudinal mount for attaching number plate wich

can be provided by the organisation. The number plate must be made out of flexible and

durable material, wich does not cause damage to the model when run over. The plate must 	be white and the numbers from 1 to 12 must be black. The number plate must be attached

to the model with two connections.

The number plate for FSR-V must be mounted on the right hand side.

The number plate for FSR-H-O must be mounted on the left hand side.

It is allowed the use the own number plate if they are according to the rules.

(4)	The dimension of number plates for classes FSR-V-H-O are as follows (see drawing 2):

Height							100 mm

Width							120 mm	The corners of the shield

Thickness		approx.			    2 mm	must be rounded off

Distance between the holes				100 mm

Distance of hole from the bottom of  plate		  10 mm

Diameter of hole					    5 mm

Drawing 2: Number plate

6.2.	Manning level of the Start Pontoon

(1)	The manning level of the positions in the FSR group is as follows:

1 chief pontoon judge.

2 assistant pontoon judges (tosupport the chief pontoon judge and observe the race).

1 official measuring the noise level.

7.	APPENDIX 1: (Guide to measure and setting up a FSR-V course)

8.	FSR-V COMPETITION COURSE AND DURATIONOF THE RACE

(1)	The competition will be held on a course as shown in drawing 3. The competition course

has to be placed so that the base line runs parallel to the starting pontoon and the centre line

is at a right angle from between start positions 6 and 7 to the centre buoy.

(2)	A competition consist of two 20 minute heats and a 30 minute final. After the first

10 minutes and every following 5 minutes there must be a verbal announcement of the

time elapsed. The time elapsed must also be displayed to the competitors.

8.1.	Drawing 3: Competition course V classes

(1)	Lapcounter and finish line have to be on the left hand side of the pontoon.

12 ------ 1 = Start positions

RB = Rescue Boat

LC = Lapcounting

8.2.	Procedures for races in the FSR-V classes

(1)	The course is sailed anti-clockwise. For every heat maximum of 12 and minimum of 3

competitors are allowed. If  more than 12 competitors have entered the competition, they

should be split into equal groups of no more than 12. The make up of the groups should be

random, taking into consideration the available crystals. This will be checked by the judges.

For the first heat the start positions are allocated by the organiser. For the second heat the

start positions are reversed (the start numbers on the boats are the same as in the first heat).

(2)	All heats in an individual class should be run consecutively with the aim that the same

weather conditions apply to all competitors.

(3)	When more than 12 competitors enter a championship a qualification races must be held in

order to decided the 12 finalist.

(4)	Before the start of each race a radio check has tob e carried out to prevent interference.

There fore all transmitters and receivers must be switched on. When it has be confirmed

That there is no radio interference it is not longer possible to protest.

(5)	After the radio check, the preparation time begins. (if the radio is not working and the

radio check is closen the competitor can not take part on that heat).

(6)	The preparation time for the FSR-V classes is 3.5 minutes. During this time the competitor

is allowed 3.5 minutes to warm up and tune the engines. During this time the model can

be place in the water but must not be released.

(7)	After the preparation time all models must be on the pontoon with the engines switched off.

Then within a short time the start position official can start the race.

(8)	The race will begin with an accoustic signal given by the start official. After the signal the

engines can be started and the models launched.

(9)	During the race you are allowed to pick up your boat by your self (assistant) the boat must 	come in with a running engine, and on his own start position place on the pontoon.

The competitor (assistant) may leave the start position to rescue the model (if the rescue 	boat bring in the boat) or to fetch spare materials. However while driving the competitor 	must not leave the start position. It is not allowed to remove the transmitter from the start 	position.

(10)	All bouys must be negotiated in accordance with the course. Touching the buoys is allowed.

Only those laps negotiated in accordance with the course are counted. Driving across the

top of the buoy the lap will not be count.

(11)	If a buoy is passed on the wrong side, it is allowed to recircle the buoy without interfering

with other competitors. If you do not recircle the buoy the lap will not be counted.

(12)	During the race each competitors laps must be displayed on a score board.

8.3.	Rules for overtaking

(1)	A slower boat can be overtaken on either side. During the overtaking manoeuvre the slower

boat must not change course or get the way of the overtaking boat. The overtaking boat can

return to the racing line when no less then three boat lengths ahead.

(2)	The faster boat is not allowed to interfere with the slower model during the overtaking

manoeuvre.

(3)	The boat on the race line which is less than 5 boat lengths from a buoy has right of way.

A manoeuvre to force a boat to pass on the side of a buoy in order to overtake is

not permitted.

Example No.1

Boat no. 1 has right of way and boats 2 and 3 try to overtake.

Boat no. 3 cuts the racing line for boat no. 1 wich results in

a lap penalty for boat no. 3.

Boat no. triest o force its’ way on the inside, in order not to

hit the buoy it will have to turn right and will cut across

boat no. 1 racing line. This results in a penalty for boat no. 2.

Example No. 2

Boat no. 2 overtakes correctly, well clear of boat no. 1.

It is at least 3 boat lengths ahead of boat no. 1 before it

returns to the racing line.

Example No. 3

Boat no. 2 cuts boat no. 1 racing line. This forces boat

no. 1 to pass the buoy on the inside to avoid a collission.

This results in a 1 lap penalty for boat no. 2.

Example No. 4

Boat no. 2 correctly leaves the inside racing line clear.

Example No. 5

Boat no. 1 has the racing line closest to the buoy

and right of way. Boats 2 and 3 must maintain their

distance from the buoy around the turn to avoid a penalty.

Example No. 6

Boat no. 1 has the racing line closest to the buoy and right

of way. Boats no. 2 and no. 3 must maintain their distance

from buoy around the turn to avoid a penalty.

8.4.	Penalties in FSR-V classes

(1)	The first occurrence of not following the rules described in paragraphs (1)-(2)-(3) 8.3.,   	where no other boat has stopped as a result of a incdent a warning (yellow card)

will be given.

(2)	The second occurrence of not following  the rules described in paragraphs (1)-(2)-(3) 8.3.,

or a more serious incident, or running over a stopped boat will be puneshed with one lap

deduction (yellow card with number 1).

(3)	The third occurrence of not following the rules described in paragraphs (1)-(2)-(3) 8.3.,

or exeptional serious incident, or causing another boat to stop will be puneshed by a two

laps deduction (yellow card with number 2).

(4)	If a model touches  a rescue boat the competitor is disqualified from that heat. The model

has to be taken out of the water immidiality.

(5)	If other models are involved in endangering, touching or collision with rescue boat, the start

position official can in their own discretion penalise the other competitors as well.

(6)	If a model is passing the rescue boat or the pontoon inside 3 metres with fast speed he will

get a Stop and Go penalty yellow safety card. The judge must be verbally and visually given

this penalty. After this the competitor have to finish his lap to taken out the model, swich of

the engine (this must be done before he/she take the boat out of the water). After this he/she 	can start again and follow the race. If the competitor get the safety card for the third time

(he/she) in the same head the boat must be bring in and can not take further part in that head.

(7)	There is no possibility of an appeal against the decicion. The start position official must 	record the penalty and the start number of the competitor.

8.5.	Basic rules in the FSR-V classes

(1)	If during a race a boat stops, it can be retriever by the rescue boat, causing minimum

disruption to the other boats. The lap on wich the boat stopped is not counted.

(2)	Boats returned by the rescue boat must resume the course from the starting position.

After the new start the laps will be added to those previously archieved.

(3)	FSR-V boats can be repaired and refuelled during a heat. Only laps completed during

the heat will be counted.

(4)	If a boat looses the number plate during the race it is allowed to complete the

commenced lap. Any laps completed after this lap without a number plate will not

be counted.

(5)	A race can be stopped by the start position official due to exeptional circumstances

(e.g. sheered off buoys). Rules for stopping a Race.

(6)	The start position official given an acoustic signal the same as the end of a race.

At the same time as the signal is given the clock which measures the duration of

the race is stopped. After the start position official has given the signal, the models

have to complete the commenced lap and this lap will be counted.

(7)	The time, from when the signal was given, untill the models pass the finish line,

must be recorded. The models have to taken from the water and the engines stopped.

(8)	Competitors and assistants have to step back from the models. Repairs are not

permitted. During the interruption in the race models can be rescued.

(9)	After resolving the cause for the interruption, the start position official will give

a start signal following the same procedure as at the beginning of the race.

(10)	The time keeping will be continue with the start signal.

(11)	If the race is stopped within the first three minutes it will be annulled and

restarted from the beginning.

(12)	If heats had to be stopped, all the laps and times have to be added together.

(13)	The end of the race is indicated by an acoustic signal. All models must after the 			signal complete the commended lap and this lap will be counted. After the final

signal the lap counters will be record the time of delay for every model passing

the finishing line. This time will be recorded with the number of laps.

8.6.	Scoring in FSR-V classes

(1)	The competition result is decided on the number of valid laps and the delay time

after deduction of penalty laps.

(2)	If there are 12 of less competitors entered for a particular class only two heats from

30 minutes have to run. The best score from the two heats will count to decide the places.

(3)	The places will be decided on the numbers of laps achevied. When there is more than

one competitor with the same number of laps, the competitor with the shorter time or

delay time will be placed higher.

(4)	In the event that a final race takes place in accordance with paragraph (3) 8.2. the placing

are as follows:

a)	The finalists are placed according to the finishing position in the final.

b)	placing of the remaining competitors will be in sequential order of the number of

laps and delay time achieved in their best qualifying heat.

8.7.	Composition of Result List in the FSR-V classes

The following items should be recorded in the result list of  a competitor in the FSR-V class:

Type, place and date of the event

Sequence of placing in accordance with paragraph 8.6.

Class

Surname, Christian name and country registration number of the competitor

Noise level result

Number of valid laps (in brackets any laps deducted) from the best heat

The delay time from the best heat

Name and registration number of the judge

Signatures of the chiefjudge

9.	FSR-H COMPETITON COURSE AND DURATION OF THE RACE

(1)	The competition will be held on a course as show in drawing 4. The competition course

has to be placed so that the base line runs parallel to the starting pontoon and the centre

line is at a right angle from between start positions 4 and 5 to the centre buoy.

9.1.	Drawing 4: Competition course FSR-H

1------8 = Start positions

LC = Start and finish line - lap counting

RB = Rescue boat

SC = Start clock

9.2.	Start clock for FSR-H classes

(1)	The start clock is designed for FSR-H races with special optical and accoustical

information and signals which the competitors use to prepare for the start of the heat.

Drawing 6:

(2)	The start clock must comply with the following:

1 turn of the hand must be 30 seconds with a precesion of approx. 1 second.

The face of the clock must show the following points: 15 seconds, 7.5 seconds,

5,4,3,2,1, seconds.

The 5 seconds segment must be shown in a contrast color.

There must be 4 red lights which are all swiched on at the beginning of preparation time.

The lights will be swiched off individually at 30 second interval.

After the last red light has gone off a yellow light will come on which indicates the

30 second time when no boats can be launched. At he end of this 30 seconds a white

light and a acoustic signal will indicate the start of the heat.

The clock hand must reach the “12 o’ clock” position at exactly the same time as the light

and acoustic signal indicate the start of the race.

The face of the clock must be white or orange, the hand must be black.

The diameter of the face of the clock must between 750 and 1000 mm.

The start clock must be able to flote so that can he positioned within the competition course.

9.3.	Procedures for races in the FSR-H classes

(1)	The course is sailed clockwise. Starting time fore the heat has to be show

on a start clock. (see drawing 6)

(2)	The models have to achieve the following number of laps within 4 minutes:

FSR-H 3.5cc	=	6 laps

FSR-H 7.5cc	=	6 laps

FSR-H 15cc	=	6 laps

FSR-H 27cc	=	6 laps

(3)	The H classes are running 2 heats on a day and  the follow order will be on this manner

3.5 J, 3.5 S, 7.5 S, 15 S, 27 S and arround again.

(4)	A heat shall be so composed that the competitors will be mixed in the heats as much as

posible. Also the place on the pontoon shall by randomly.

(5)	A heat must have a minimum of 4 competitors and maximum of  8 competitors. Each

competitor must run at least 4 heats. If there are more than 8 competitors entered in a class,

a final must be run in accordancce with paragraph (4).

(6)	8 competitors with the highest scores from the heats qualify for the final. For the final at

least 4 heats must be run. The best placed competitor will occupy start position 1, the second

best placed start position 2, the third best placed start position 3, the fourth best placed

start position 4 etc. until the eight placed, who will occupy start position 8.

(7)	Before the start of each heat a radio check has to be carried out to prevent interference.

There for all transmitters and recievers must be switched on. When it has been confirmed

that there is no radio interference it is not longer possible to protest (8.2. (5) page 24).

(8)	Each race consists of three independent phases:

Preparation time (Pite time) 2 minutes

Control time (Milling time) 30 seconds

Course time (Race time) 4 minutes

(9)	During preparation time engines are started,and the boats launched. If a competitor starts

an engine after the preparation time, this race will not count. Races can not be repeated.

Preparation time must not be delayed or cancelled, unless in exeptional circumstances

At the judges discretion (e.g. problems on the race course).Models can be adjusted during 	the preparation time, however the competitor is not allowed to leave the start position.

(10)	At the start of control time no further boats can be launched.

(11)	The competitor must drive the boats around the course or the special lay-by zone allocated

by the competition management, so that all competitors can cross the start line at the end of

control time. Boats must drive the course in the clockwise direction.

(12)	During the last 15 seconds of the control time in order to ensure the safety of all the boats,

the models must keep in a straight line after passing buoy No. 6. Zigzagging across the

course, course changes in excess of 45 degrees in order to avoid crossing the start line

early etc., are not allowed and are penalised with one extra lap.

(13)	The end of the control time indicates the startof the race time, regardles of where the boats

are on the course.

(14)	Models crossing the startline immidiately before the end of the control time have a false

start and must there for complete an extra lap.

(15)	Durend the preparation time, control time, racing, missing a bouy and there fore cutting

the course is penalised by one extra lap.

(16)	The competitor whose boat crosses the line first after completing the required number of

laps and taking into account any penalties (additional laps) is the winner.

(17)	In the event that no boat completes the required laps within the 4 minutes run time, the

race is discounted.A repetition of the race is not permitted.

(18)	Boats, which have not completed the required number of laps, recieve 25 points.

(19)	After a competitor has completed the required number of laps they must remove the boat

from the water. The start position official must order to quit the race course.

(20)	If  the start position official considers that there are boats on the race course which will

not able to complete the race in the racing time remaining, they can request them to take

their boats out of the water. The point given will be the same as in case when the race is

not completed (25) points.

(21)	Re-run of race (heat). If a race in FSR-H classes has to re-run becouse it was interrupted, 	only the boats still running at the point the race is stopped should have the right to restart.

The boats wich have stopped during the orginal race get 25 points.

(22)	Heats must be organised so that no one competitor will have to take part in two

consecutive races.

(23)	Each race must be run in accordance with the rules specified in section 9.4.

9.4.	Basic rules and penalties in the FSR-H classes

(1)	Falling to comply with the following rules could result in a disqualification from one

heat or entire competition.

9.4.1.	Left turns

(1)	Exessive left turns on the course are not permitted, exept when giving way or to avoid

collission.

(2)	Penalised by one extra lap will be in the following cases:

Left turn in exess of 45 degrees, when a competitor by turning to the left endangers

another model.

(3)	Cousing damage to another boat, which will prevent it from being used in the competition

will result in a disqualification from that heat.

9.4.2.	Right of way

(1)	Reliable turning and steering techniques as well as sporting fairness are provisions for the

proper sailing/use of the race course.

(2)	The normal racing line is the line closest to the outline of the course. Boats on the racing

line have right of way.

(3)	A boat on a normal racing line has the right to maintain its course.

(4)	A boat overtaking the boat ahead, which is on the same racing line must be at least

3 boat lengths ahead before it has the right to way.

(5)	Penalised by one extra lap will be in the following cases:

Not following the rules specifying the right of way

Preventing another boat from overtaking by a zigzagging, S-turns,etc.

9.4.3.	Negotiating/passing the buoys

(1)	Each buoy on the race course must be negotiated on the outside. An exeption can only

be made by the start position official, if it would benefit the race situation or in order to

avoid a collision. Driving across the top of the buoy will not be counted.

(2)	Buoy penalties are given by the assistant pontoon judges. It is not posible to

protest their decision.

(3)	If a competitor cannot steer their boat properly they will recieved a warning.

If their driving has not improved, they will be disqualified from this head.

(4)	Penalised by one extra lap will be in the following cases:

a) Passes a buoy on the inside (one penalty lap for each buoy, also in the control time)

b) Driving inside of the oval race course

c) Cutting or crossing the race course

d) Driving through the middle of the race cours

e) To fast speed on the pontoon inside 3 metres a yellow safety card

f) When the third penalty has been issued (in the same heat) the competitor will be told to

bring the boat in and take no further part in that heat.

9.5.	Rules for overtaking in the FSR-H classes

Overtaking in accordance with paragraph 9.4.2. is allowed on the entire course.

The following examples are only guidance for the judges and can not be cited by

competitors in a possible protest. In the situations described below serious danger

could a rise to other boats or spectators. In this case the start position official can order

the competitor, cousing the danger, to discontinue the race. The competitor will be

disqualified  for this heat and will receive no points.

Example No. 1

Example No. 2

Example No.3

Example No. 4

Example No. 5

9.6.	Calculation of final results in the FSR-H classes

(1)	In FSR-H classes, each competitor recieves the following points according to the

place achieved:

1. Place						= 400 points

2. Place						= 300 points

3. Place						= 225 points

4. Place						= 169 points

5. Place						= 127 points

6. Place						=   96 points

7. Place						=   72 points

8. Place						=   54 points

Race not completed					=   25 points

Boat did not pass the starting

line after the starting signal.				= No points

(2)	In cases of equal points there should be arun off in the following cases:

a)	To select a competitor for the final

b)	In the final, to decided places 1, 2 or 3

The run off will be held after the completion of the heats or after the finals.

(3)	The final result of the competiton is the sum of all points achieved in all heats unless

finals are held.

(4)	If a final takes place, the results will be as follows:

a)	All finalist are placed according to the total of points achieved during the final.

b)	The remaining competitors are placed according the total of points achieved

during the qualification heats.

9.7.	Composition of result list in the FSR-H classes

The following items should be recorded in the result list of a competitor in the

FSR-H class:

Type, place and date of the event

Class

Surname, Christian name and country registration number of the competitor

Noise level result

Result of each race (points, penalty laps)

Total points scored

Total penalty laps

Name an d registration number of the judge

Signature of the chief judge

10.	FSR-O COMPETITION COURSE AND DURATION OF THE RACE

(1)	The competition will be held on a course as shown in drawing 5. The competition course

has to be placed so that the base line runs parallel to the starting pontoon.

10.1.	Drawing 5: Competition course FSR-O

(2)	Lapcounter and finish line have to be on the left hand side of the pontoon.

1------10 = Start positions

LC = Lap counting

RB = Rescue boat

SC = Start clock

(3)	The startclock is designed for FSR-O races with special optical and accoustical

information and signals which the competitors use to prepare for the start of the heat.

10.2.	Start clock for FSR-O races

(1)	The start clock must be comply with the following:

1 turn of the hand must be 30 seconds with a precision of approx. 1 second.

The face of the clock must show the following points, 15 seconds, 7.5 seconds,

5, 4, 3, 2, 1, seconds. The 5-second segment must be show in a contrast color.

There must be 4 red lights, which are all switched on at the beginning of preparation time.

The lights will be switched off individually at 30 second intervals. After the last red light has

gone off a yellow light will come on which indicates the 30 seconds control time when no

boats can be launched. At the end of this 30 seconds a white light and a acoustic signal will 	indicate the start of the heat. The clock hand must reach the “12 o’clock” position at exactly

the same time as the light and accoustic signal indicates the start of the race.

The face of the clock must be white or orange, the hand must be black.

The diameter of the face of the clock must be between 750 and 1000 mm. The start clock 	must be able to float so that it can be positioned within the competition course.

10.3.	Procedures for races in the FSR-O classes

(1)	The course is sailed clockwise. Starting time before the heat has to be show

on a start clock (see drawing 6:)

(2)	The Offshore classes are running 2 heats, heat 1 and 2 on a day and the follow order will

be on this manner 3.5 J, 3.5 S, 7.5 J, 7.5 S, 15 J, 15 S, 27 S, 35 S, and around again.

(3)	For heat 3 and 4 the start positions are reversed ( the start numbers on the boat are the same

as in heat 1 and 2).

(4)	A heat must have a minimum of 4 and maximum of 10 competitors. Each competitor must

run at least 4 heats. If there are more than 10 competitors entered in a class, a final must be 	run.

(5)	10 competitors with the highest scores from the heats qualify for the final. For the final one

heat is to be run. The best placed competitor will be occupy start position 1, the second best

placed start position 2, the third best placed start position 3, and so on till place 10.

(6)	Before start of each heat a radio check has to be carried out to prevent interference.

There fore all transmitters and receivers must be on. When it has been confirmed that there

is no radio interference it is not longer possible to protest. (8.2. (5) page 24).

(7)	Each race consists of three independent phases:

Preparation time (Pit time) 2 minutes

Control time (Milling time) 30 seconds

Course time (Race time) 8 minutes for qualification and 12 minutes for final.

(8)	During preparation time engines are started, and the boats launched. Races cannot be 	repeated. Preparation time must not be delayed or cancelled, unless in exeptional

circumstances at the judges discretion (e.g.problems on the race course). Models can be

adjusted during the preparation time, however the competitor is not allowed to leave the

start position.

(9)	During the control time no further boats can be launched. During the course time the

competitors are allowed for after start.

(10)	The competitor should have 1 minimum milling lap. If the boat not is in the water at the

white light the judge will be given the competitor 1 penalty lap.

(11)	The competitor must drive their boats around the course or the special lay-bay zone

allocated by the competition management,so that all the competitors can cross the start line

at the end of control time.

(12)	During the last 15 seconds of the control time in order to ensure the safety of all boats, the 	models must keep in a straight line after passing buoy No. 6. Zigzagging across the course, 	course changes in exess of 45 degrees in order to avoid crossing the start line early etc., are

not allowed and are penalised with one lap deduction.

(13)	The end of the control time indicates the start of the race time, regardless of where the

boats are on the course.

(14)	Models crossing the start line immediately before the end of  control time have a false start

and must there fore complete an extra lap.

(15)	FSR-O boats can be repair and/off refuled during a heat. Only laps completed during the

heat will be counted.

(16)	For repairing or refuelled the boat must come in with a running engine, on his own		start position on the pontoon.

(17)	During the race time you may leave the start position to pickup fetch or spare materials.

However while driving the competitor must not leave the start position. It is not allowed

to remove the transmitter from the start position.

(18)	All buoys must be negotiated in  accordance with the course. Touching the buoys is allowed,

only those laps negotiated in accordance with the course are counted.

(19)	If a buoy is passed on the wrong side, it is allowed to recircle the buoy without interfering

with other competitors. If you do not recercle the buoy the lap will not be counted.

(20)	A slower boat can be overtaken on either side. During the overtaking manoeuvre the slower

boat must not change course or get the way of the overtaking boat. The overtaking boat can 	return to the racing line when no less the three boat lengths ahead. The faster boat is not

allowed to interfere with the slower model during the overtake manoeuvre.

(21)	The boat on the race line, which is less than 5 boat lenghts from a buoy, has right of way.

A manoeuvre to force a boat to pass on the inside of a buoy in order to overtake

is not permitted.

(22)	During the race each competitor laps must be displayed on a score board.

(23)	If a boat looses the number plate during the race it is allowed to complete the commenced	lap. Any laps completed after this lap without a number plate will not be counted.

(24)	A race can be stopped by the start position official due to exeptional circumstances (e.g.

sheered off buoys). Rules for stopping race.

(25)	The start position official gives an accoustic signal about the same as the end of a race.

At the same time as the signal is given the clock which measures the duration of the race

is stopped. After the start position official has given the signal, the models have to

complete the commenced lap and this lap will be counted.

(26)	The time, from where the signal was given, untill the models pass the finish line, must be

recorded. The models have to be taken from the water and the engines stopped.

(27)	Competitors and assistants have to step back from the models. Repairs are not permitted..

During the interruption in the race models can be rescued.

(28)	Rescued boats are not allowed to restart.

(29)	After resolving the cause for interruption, the start position official will give a start signal.

The time keeping will continue with the start signal.

(30)	If the race is stopped within the first three minutes it will be annulled and restarted

from the beginning.

(31)	If a heat had to be stopped, all laps and time have to be added together.

(32)	The end of the race is indicated by an acoustic signal. All models must after the signal

complete the commenced lap and this lap will be counted. After the final signal the

lap counters will record the time of dealy for every model passing the finishing line.

This time will be recorded with the number of laps.

10.4.	Basic rules and penalties in the FSR-O classes

(1)	Falling to comply with the following rules result in a disqualification from one heat

or entire competition.

(2)	In cases of unfair behaviour, interference with other competitors, not following the rules

or endangered spectators(e.g. collision with the starting pontoon) to fast within 3 metre

from the pontoon a yellow safety card. The start position official can pronounce the 	following penalties.

(3)	The first occurrence of not following the rules described in paragraphs (19-20-21) 10.3.,

where no boat has stopped as a rusult of the incident a warning (yellow card) will be given.

(4)	The second occurrence of not following the rules described in paragraph (19-20-21) 10.3.,

or a more serious incident, or running over a stopped boat will be punished with a one lap 	deduction (yellow card with number 1).

(5)	The third occurence of not following the rules described in paragraph(19-20-21) 10.3.,

or a exceptionally serious incident, or cousing another boat to stop will be punished by a

two lap deduction (yelow card with number 2).

(6)	The fourht occurence of not following the rules described in paragraph (19-20-21) 10.3.,

or exceptionally inconsiderate behaviour of a competitor will be puneshed by

disqualification (red card). The model has to be taken out of the water immediately.

(7)	The yellow safety card will be given one penalty lap off. If the competitor get the safety

card for the third time (in the same heat) he has to take out his boat and can not take part 	further on in that heat. The competitor must verbaly and visually  notified of a penalty.

There is no possibility on a appeal against the decision. The start position official must

record the penalty, and the start number of the competitor.

10.4.1.	Left turns

(1)	Exessive left turns on the course are not permitted, exept when giving way or to avoid.

Minor steering corrections to the left, or to overtake other boats are allowed.

(2)	Penalised by one lap deduction will be in the following cases:

a) Left turn in exess of 45 degrees, when a competitor by turning to the left endangered

another model.

(3)	Cousing damage to another boat, which will prevent it from being used in the

competition will result in a disqualification from that heat.

10.4.2.	Right of way

(1)	Reliable turning and steering techniques as well as sporting fairness are provisions

for the proper sailing/use of the race course.

(2)	The normal racing line is the line closest to the outline of the course. Boats on the

racing line have right of way.

(3)	A boat on a normal racing line has the right to maintain its course.

(4)	A boat overtaking the boat ahead, which is on the same racing line must at least 3 boat

lenghts ahead before it has the right of way.

(5)	Penalised by one lap deduction will be in the following cases:

a) Not following the rules specifying the right of way preventing another boat from

overtaking by zigzagging, S-turns, etc.

10.4.3.	Negotiation- Passing the buoys

(1)	Each buoy on the race course must be negotiated on the out side. An exeption can only be

made by the start position official, if it would benefit the race situation or in order to avoid

a collision. Driving across the top of the buoy will not be counted.

(2)	Bouy penalties are given by the assistent pontoon judges. It is not posible to protest

their decicion.

(3)	If a competitor cannot steer their boat proporly they will received a warning. If their driving

has not improved, they will be disqualified from this heat.

(4)	Penalised by a one lap deduction will be in the following cases:

Passes a buoy on the inside (the boat has not recircle the buoy)

Driving inside the oval course

Cutting or crossing the race course

To fast speed on the pontoon inside 3 metres, a Yellow safety card will given a one lap 	deduction. When the third penalty has been issued (in the same heat) the competitor wil be 	bring the boat in and take not further part in that heat.

10.5.	Rules for overtaking in the FSR-O classes

(1)	Overtaking in accordance with paragraph 10.4.2. is allowed on the entire course.

The following examples are only quidance for the judges and can not be cited by

competitors in a possible protest. In the situations described below serious danger

could a rise to the boats or spectators. In this case the start position official can order

the competitor, causing the danger, to discontinue the race. The competitor will be

disqualified for this heat and will receive no laps.

Examle No. 1

Example No. 2

Example No. 3

Example No. 4

Example No. 5

10.6.	Scoring in FSR-O classes

(1)	The competition result is decided on the numbers of valid laps and the delay time after

deduction of penalty laps.

(2)	The best three of four heats will be counted together for qualification scorse.

(3)	If there are 10 or fewer competitors entered for a particular class only qualification has

to be run. This will be the finally result.

(4)	The place will be decided on the number of laps achieved. When there is more than one

competitor with the same number of laps, the competitor with the shorter delay time will

be placed higher.

(5)	In the event that a final race take place in accordance with paragraph (2 – 3) 10.3., the

places are as follows:

a) The finalist are placed according to their finishing position in the final.

b) Placing of the remaining competitors will be in sequental order the number of laps and

delay time achieved in their qualifying heat.

10.7.	Composition of result list in the FSR-O classes

The following items should be recorded in the result list of a competitor in the FSR-O class:

Type, place and date of the event

Sequence of placing in accordance with paragraph 10.7.

Class

Surname, Christian name, country and registration number of the competitor

Number of valid laps (in brackets any lap deducted) from each heat and total

The delay time from each heat and total

Name and registration number of the judge

Signature of the chief judge

# Text boxes

2

1

3

2

1

1

2

1

2

1

2

X

1

2

3

Boat No. 1 has  the right of way.  and boats No.2 and No.3 try to overtake.

Boat No.2 cuts the racing line for boat No.1, which results in a one extra lap Boat No. 3 tries to force its way on the inside, in order not to touch the buoy the boat No. 3 will have to turn left and will cut across boat No.1’s racing line.  This manoeuvre will result in one extra lap.

Boat No.2 overtakes correctly, it is at least 3 boat lengths ahead of boat No.1 before it returns to the racing line.

Boat No.2 receives a one lap penalty because it forced boat No.1 to pass the buoy on the inside in order to avoid collision.

Boat No.2  correctly leaves the inside racing line clear.

Boat No.1 leaves the inside racing line clear because it turned wide. It allows boat No.2 to overtake by making a tighter turn.  In position X the boat No. 2 has the right of way.

Boat No. 1 has  the right of way.  and boats No.2 and No.3 try to overtake.

Boat No.2 cuts the racing line for boat No.1, which results in a one lap deduction. Boat No. 3 tries to force its way on the inside, in order not to touch the buoy the boat No. 3 will have to turn left and will cut across boat No.1’s racing line.  This manoeuvre will result in a one lap deduction.

Boat No.2 overtakes correctly, it is at least 3 boat lengths ahead of boat No. 1 before it returns to the racing line.

Boat No.2 receives a one lap deduction because it forced boat No.1 to pass the buoy on the inside in order to avoid collision.

Boat No.2  correctly leaves the inside racing line clear.

Boat No.1 leaves the inside racing line clear because it turned wide. It allows boat No.2 to overtake by making a tighter turn.  In position X the boat No. 2 has the right of way.